## Slide 1
Improve Productivity using OpenBIM IFC for BASIX compliance
Online Meeting
14th January 2026
John Mitchell: CQR
Scott Beazley: GeometryGym
v1

## Slide 2
Digital possibilities for efficiency and productivity gain
An example from housing in NSW
NCC structure
NSW variations
Section H6 Energy Efficiency for residential buildings – BASIX (Building Sustainability Index)
Current BASIX input method
A large amount of data is required to populate the website data fields manually with keyboard and mouse
Project proof of concept
Use project information contained in digital 3D design file to automate the population of data fields
Embed data within the model objects and align to BASIX data fields
Verification method to check model data

## Slide 3
Trust of digital information from 3D models to:
Contain Project data
Achieve Compliance
Reduce Risk
Avoid Duplication
Eliminate Inconsistency
Eliminate effort
Architect\ Designer
Design components
Object data
Regulatory Compliance
NCC\BCA\local requirements
Project data
Design components
Object data
Product supplier
Component data
Regulatory Assessment
Specific project data
NCC\BCA\local requirements
Design components
Object data

## Slide 8
NCC structure: NSW variation
Section H & J for residential buildings
This includes BASIX
Online submission
Aim to achieve minimal for water usage, energy consumption and maximise thermal comfort etc.
Once achieve minimum level then can generate a BASIX Certificate from website
What data does the BASIX require?
Building and site areas
Fabric specifications
Appliance type
Window areas, glazing specification, orientation, shading
Information already contained in 3D models

## Slide 9
Relevance for other code compliance uses
Parts of the puzzle
Defined

## Slide 13
Improving Productivity with Open BIM, IFC and IDS
Submission of a BASIX assessment is currently a complex web-based task requiring manually filling in over 200 information items, requiring tedious preparation, duplication of tasks etc.
We demonstrate IDS - the new way of validating information content in a building model.
IDS offers a simpler process,
integration with the BIM authoring process and
actually provides more accurate data to assess the performance requirements of BASIX.
The talk will explain the role of IDS and provide a demonstration of an actual residential building using a prototype developed by Dion Moult.

## Slide 14
Sample of required BASIX data
Submission of a BASIX assessment is currently via a web-based task requiring manually entry

## Slide 15
Submission of a BASIX assessment is currently a complex web-based task requiring manually filling
Sample of required BASIX data

## Slide 16
Data within 3D models
Revit 3D model

## Slide 17
Data within 3D objects
Revit 3D model
IFC 3D model in Solibri Model Checker

## Slide 18
specifying the IFC data…in ArchiCAD model
Landscape Plan

## Slide 19
Improving Productivity mapping data for BASIX use
Mapping of BASIX terminology to IFC standard and custom properties and Property Sets

## Slide 20
Improving Productivity mapping data for BASIX use
Mapping of BASIX terminology to IFC standard and custom properties and Property Sets

## Slide 21
Improving Productivity mapping data for BASIX use
Mapping of BASIX Floor Types terminology to IFC standard and custom properties and Property Sets

## Slide 22
Improving Productivity mapping data for BASIX use
Mapping of BASIX Floor Types terminology to IFC standard and custom properties and Property Sets

## Slide 23
Mapping of BASIX terminology to IFC standard and custom properties and Property Sets
Improving Productivity mapping data for BASIX use

## Slide 24
Mapping of BASIX terminology to IFC standard and custom properties and Property Sets
Improving Productivity mapping data for BASIX use

## Slide 26
Back end coding

## Slide 27
Back end coding

## Slide 28
Back end coding

## Slide 29
Back end coding

## Slide 30
Improving Productivity using IDS

## Slide 31
BASIX magic
Running the model data extract to BASIX website

## Slide 41
Potential next steps
Seek ABCB, NABERS, BASIX and industry support to invest in a complete solution
We have already a working team, and need government, product manufacturers and industry associations to support the concept as a national initiative
Our prototype highlights the productivity gain to both submitters and assessors as the model becomes a reliable, single source of data required by BASIX.
This project can introduce to Australian building authorities the benefits of model-based code checking adding a further layer of efficiency addressing the current low productivity of the building industry
A bSDD library of BASIX specific terms can be created to support web access and project consistency.

## Slide 42
Relevance for code compliance other uses
Adopting the IFC model solution
facilitates incremental submission and testing during design phase
enhances services integration with the architectural models
provides BASIX with precise (geo-referenced) geometric, spatial & performance measures
solution can be expanded for other regulatory compliance
Similarities with DA submission via the internet
Parallel compliance method proposed for digital submission
Aim for 80% of project data to be accessed from the digital model
Some data for manual entry
Digital connections to cost, carbon calculations, asset management also available

## Slide 43: Thank You…..any questions?
Improve Productivity using OpenBIM IFC for BASIX
Online meeting
14th January 2026
John Mitchell: CQR
Scott Beazley: GeometryGym
scott@geometrygym.com
john.mitchell@cqr.net.au

## Slide 44
Relevance for other code compliance uses
Parts of the puzzle
Defined data for model and model objects
IDS for machine and human readable briefing
Data added to model
Export to IFC
Verification and validation of model data: Present, valid, correct.
Load into website

## Slide 45
Components for creating the Prototype…
Our next steps were to
develop the IDS specification - in prototype - for most of Steps 1 - 3 of the BASIX portal
develop working code (using ifcOpenShell and Python) to generate the web data from the IDS specification
using 2 residential models in Revit and ArchiCAD create test ifc exports using Blender’s IDS reporter, Solibri etc as requirements were specified
As all this came to a point of definition Dion extended his Blender IFC native authoring app to connect the model data to a dummy BASIX web portal

## Slide 46
spec = add_spec("1.2", "Project Name”)
spec.applicability.append(ifctester.ids.Entity(name=“IFCPROJECT"))
spec.requirements.append(ifctester.ids.Attribute(name="LongName"))
spec = add_spec("1.2", "Plan Type", "NSW Plan type shall be provided to uniquely identify the land Title")
spec.applicability.append(ifctester.ids.Entity(name="IFCSITE"))
restriction = ifctester.ids.Restriction(options={"pattern": "(SP|DP).+"})
add_property(spec, "Pset_LandRegistration", "LandTitleID", "IFCIDENTIFIER", restriction)
spec = add_spec(
"1.2", "Property Address", "Address information shall be provided to uniquely identify the project location"
)
spec.applicability.append(ifctester.ids.Entity(name="IFCSITE"))
add_property(spec, "Pset_Address", "Town", "IFCLABEL")
add_property(spec, "Pset_Address", "PostalCode", "IFCLABEL")
add_property(spec, "Pset_Address", "Region", "IFCLABEL")
add_property(spec, "Pset_Address", "Country", "IFCLABEL")
an IDS Specification…

## Slide 47
an IDS Specification…

## Slide 48
getting an IDS report…

## Slide 49
Blah, blah, blah
  Blah, blah, blah

## Slide 50
Blah, blah, blah
  Blah, blah, blah

## Slide 51
Blah, blah, blah
  Blah, blah, blah

## Slide 52
Improving Productivity using IDS
As all BASIX submitters know, BASIX requires detailed environmental, water usage, waste, electrical data - the IFC source model needs to be multi-disciplinary!
Our small examples highlight the benefit to modelling requiring authoritative, defensible data in the emerging context of embodied carbon and certified building product data.
Smart digital access to property & land data, council zoning, government utility services, climate zones… would make the model more robust
Adopting the IFC model solution
facilitates incremental submission and testing
enhances services integration with the architectural models
provides BASIX with precise (geo-referenced) geometric, spatial & performance measures
solution can be expanded for other regulatory compliance

## Slide 53
Improving Productivity with Open BIM, IFC and IDS
https://evitat.com.au/
https://pp.planningportal.nsw.gov.au/development-and-assessment/basix/about-basix/dwelling-types/multi-dwelling
Multi-dwelling | Planning Portal - Department of Planning and Environment
NSW Planning Portal Spatial Viewer
https://www.planningportal.nsw.gov.au/spatialviewer/#/find-a-property/address